## Slide 1
IDEAS KICKOFF · IIT BOMBAY
AgriRover
A production-intent agricultural scouting rover: dual-controller firmware, on-device AI inference, and a fully parametric CAD build.
2
CONTROLLERS
42
CAD PARTS
12,137
LINES OF CODE
Vivek Kumar Gupta · Shreyash Wagh · Hitanshu Kapadiya · Pritish Nandy
01/10

## Slide 2
WHAT EXISTS TODAY
A built system, not a concept sketch
Shipped in this repository
ESP32 firmware (PlatformIO + FreeRTOS) for drive, sensing, dosing and MQTT
71 Raspberry Pi Python modules: AI inference, EKF pose fusion, path planning
A ROS 2 package with sensor, drive, AI and mission nodes
Fusion 360 script that generates the whole rover to scale
11 pytest modules covering AI interfaces, navigation, data and stop logic
REPOSITORY SCALE
files
116 C++ / Python source files
lines
12,137 across firmware, pi, ros2, cad
docs
11 design documents in docs/
BOM
110 components + 15 gap-audit items
training
3 Colab notebooks + dataset builder
deploy
systemd, MQTT TLS, Pi hardening
SOURCE README.md
02/10

## Slide 3
COMMERCIAL HYPOTHESIS
Tomato crop-protection, Narayangaon/Junnar
Weekly repeatable sentinel sample and trap read → count and geotag suspected problems → compare against an economic threshold → trigger a full-row scan only when risk justifies it → agronomist-reviewed action → record treatment and pre-harvest interval → revisit and verify.
Why this cluster
2023-24 tomato area: Nashik 22,040 ha, Pune 4,772 ha, Ahmednagar 4,324 ha, Solapur 4,072 ha
KVK Narayangaon provides local agronomy; a tomato FPO aggregates the route
Concentration dense enough to test operating economics, not just technology
SCOPE LIMITS STATED IN THE REPO
pilot v1
pesticide application stays manual
NPK probe
not used to prescribe fertilizer
500 ml tank
spot treatment only, not full-field
category
not a universal farm robot
SOURCE research/AGRIROVER_MARKET_ADOPTION_RESEARCH.md README.md
03/10

## Slide 4
SYSTEM ARCHITECTURE
Two controllers, split by timing guarantee
REAL-TIME TIER
board
ESP32 DevKit V1 (WROOM-32)
runtime
FreeRTOS, both cores used
core 1
driveTask - motor PWM, obstacle reaction
core 0
sensorTask - NPK, dosing, MQTT publish
signalling
FreeRTOS EventGroup, not volatile bool
INFERENCE TIER
board
Raspberry Pi 5 + Hailo-8 AI HAT+
throughput
26 TOPS accelerator
fallback
Pi 4 + Coral USB Edge TPU
workload
obstacle, weed, leaf-disease paths
services
evidence capture, dashboard, OTA
Command link is HMAC-authenticated and encrypted · heartbeat timeout 1500 ms halts the rover · 10 s lockout after repeated auth failures
SOURCE README.md firmware/include/config.h
04/10

## Slide 5
FIRMWARE · ACTUATION
Drive and servo PWM on separate timers
TANK DRIVE - 2X BTS7960 (IBT-2)
GPIO
19 / 21 left, 22 / 23 right
direction
PWM on RPWM fwd, LPWM rev
enable
R_EN + L_EN tied high to 3.3 V
PWM
LEDC 1 kHz, 8-bit, duty 0-255
SG90 SWEEP MOUNT
GPIO
27, LEDC channel 4 → timer 2
frame
50 Hz, 16-bit resolution
range
duty 1638 (0°) → 8192 (180°)
startup
centred at 90°
Channel 4 is deliberately on timer 2 so the servo's 20 ms frame can never collide with the 1 kHz drive PWM on timers 0 and 1. Moving from L298N to BTS7960 freed GPIO 32/33.
SEQUENTIAL DOSING STATE MACHINE — MOTORS HELD STOPPED WHILE THE PROBE IS IN SOIL
pre-soak
1500 ms
extend
4000 ms
dwell
800 ms
micro-dose
1500 ms
retract
4000 ms
SOURCE firmware/include/pins.h firmware/src/servo.cpp firmware/include/config.h
05/10

## Slide 6
MECHANICAL DESIGN
Double-decker chassis, 320 × 450 mm
Top & mast — GPS, camera, antenna
Z 257+
Sun canopy
Z 254-257
Upper deck — compute, sensors, UI
Z 158-162
Lower deck — power, drive, fluid
Z 64-68
Underside — ultrasonics, actuator, NPK probe
Z -30
FUSION 360 GENERATOR
input
docs/mechanical-layout.md is source of truth
output
42 named, colour-coded components
tree
6 assembly groups, browser mirrors the build
origin
chassis front-left corner, +Y toward rear
Layout rules that drove the stack
Fluid sits below electronics so leaks drain away
MPU6050 at centre of gravity; GPS and LoRa on the mast, clear of BTS7960 RF noise
Battery and tank low and centred for stability on uneven ground
SOURCE docs/mechanical-layout.md cad/AgriRoverPrototype/AgriRoverPrototype.py
06/10

## Slide 7
SENSING & SAFETY
Layered stop logic and a verified pin map
SENSING BUSES
RS485
NPK probe via MAX485, GPIO 17/16/4
analog
moisture 34, VBAT 35, TDS 36 (ADC1)
1-wire
DHT22 ambient on GPIO 14
UART1
GPS Neo-6M, RX 39 / TX 15 for RTCM
relays
pump 26, actuator 13, polarity 2
I2C
MPU6050, ADS1115, PCF8574, VL53L1X
STOP LAYERS (DESIGN CONTROLS)
proximity
VL53L1X time-of-flight
vision
obstacle inference on device
attitude
IMU tilt threshold
link
heartbeat watchdog, 1500 ms
motor
stall detection via ACS712
manual
E-STOP on the upper deck + Telegram /stop
GPIO 34/35/36/39 are input-only, so every analog sensor is placed on ADC1. GPIO 15 is a strapping pin whose required boot level matches an idle UART TX line, which is why GPS TX can safely live there.
SOURCE firmware/include/pins.h README.md
07/10

## Slide 8
HONEST STATUS
What is built vs. what is proven
VERIFIED IN REPOSITORY
Firmware, Pi services, ROS 2 nodes, CAD, wiring and BOMs
Simulation that runs with no hardware attached
Automated test suite over AI interfaces and stop logic
Encrypted, authenticated Pi ↔ ESP32 command link
Model OTA and active-learning frame capture
NOT YET ESTABLISHED
Crop-detection accuracy on local tomato classes
Productive acres per day and route density
Field reliability and ruggedness
Chemical reduction, yield protection, rupee savings
Willingness to pay and payback period
The README states this explicitly. Nothing in this deck claims a field result.
SOURCE README.md research/AGRIROVER_MARKET_ADOPTION_RESEARCH.md
08/10

## Slide 9
NEXT MILESTONES
Validation gates before any paid launch
01
Supervised traversal
Physical drive tests with the layered stop logic active in a real row.
02
Local tomato data
Collect and label local classes; held-out per-class validation.
03
Hailo export path
Compile and benchmark the model chain on the Hailo-8 accelerator.
04
Row navigation
Camera-based row following and boundary behaviour beyond GPS geotags.
05
12-grower pilot
Paired pilot with KVK / agronomist review and calibrated measurement.
Repo analysis also flags open engineering items to close first: a 45× flow-configuration conflict, and a savings tracker that currently mixes incompatible units.
SOURCE research/AGRIROVER_MARKET_ADOPTION_RESEARCH.md README.md
09/10

## Slide 10
TEAM
IIT Bombay · Mechanical Engineering
Vivek Kumar Gupta
25B2269
B.Tech 2029 · Uttar Pradesh
Shreyash Wagh
25B2227
B.Tech 2029 · Nashik, Maharashtra
Hitanshu Kapadiya
25B2228
B.Tech 2029 · Gujarat
Pritish Nandy
—
Team member
github.com/aman123825/agrobot
Roll numbers and details for the first three are from IDEAS_team_members.csv; the repository holds no record for Pritish Nandy, so no details are asserted.
10/10